## Slide 1: Computer Organization and Architecture – Let’s solve these.
Shriram K Vasudevan
Session – 15

## Slide 2: Q.No. 1
Write the following expression using 4 address format, 3address format, 2 address format,1 address format and 0 address format. a = b + c ; # this is the question folks.

## Slide 3: You work this out!
  Write the following expression using 4 address format, 3address format, 2 address format,1 address format and 0 address format x=(y+d)/(d+3)
  You folks try this and get me answer.

## Slide 4: Q.NO. 2
Give the register transfer notations for the following MIPS Instructions. (It could be asked as RTN or RTL also)
  LW $t2,100($s2) $t2<-mem[100+$s2]
  SW $t3,32($s2) mem[32+$s2]<-$t3
  beq $t1,$t3,8 if $t1==$t3 goto (pc+4)+8
  addi $t1,$t2,32 $t1<-$t2+32

## Slide 5: Q.NO. 3
For the following MIPS INSTRUCTIONS give the RTL equivalents, addressing modes.
or $s2,$t1,$t2 $s2<-$t1 OR $t2 - Register addressing mode
sw $t3,12($t0) mem[12+$t0]<- $t3 - Base/displacement addressing

## Slide 6: Q.NO. 4
Decode the instruction (010f8020)16
0000 0001 0000 1111 1000 0000 0010 0000 = 32 bits (Length)
Let us decode:
0000 0001 0000 1111 1000 0000 0010 0000
Ans: add $16, $8, $15 == add $s0, $t0, $t7
registers $s0 to $s7 map onto registers 16 to 23, and registers $t0 to $t7 map onto registers 8 to 15.

## Slide 7: Q. NO. 5
Decode it yourself.
Decode the instruction (022f8020) 16
registers $s0 to $s7 map onto registers 16 to 23, and registers $t0 to $t7 map onto registers 8 to 15.

## Slide 8: Q. NO. 6
Encode the following instructions in binary. Also write the RTL for each instruction
add $t1,$s0,$s1
$t1<-$s0+$s1

## Slide 9: Q. NO. 7
Encode the following instructions in binary. Also write the RTL for the instruction presented.
and $s1,$t1,$t2 RTL : $s1 <-reg $t1 & reg $t2

## Slide 10: Q.No.8
Mention the status of control signals for the below operation
ADD $s1, $s2, $s3
RegDst | ALUSrc | Memto Reg | Reg Write | Mem Read | Mem Write | Branch | ALUOP1 | ALUOP2
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0

## Slide 11: Q.No. 9
Mention the status of the control signals for the below instruction
LW $t0, 32($t1)
RegDst | ALUSrc | Memto Reg | Reg Write | Mem Read | Mem Write | Branch | ALUOP1 | ALUOP2
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
For you to solve!
Find the status of control signals for any SW operation.

## Slide 12: Q. No. 10
Write the MIPS equivalent for the following C Code.

## Slide 13: Q. NO. 10
You work this out.
Write the MIPS equivalent for the following C Code.
1. a=(b-d)+2;
2. while(a!=b)
{
  c=c+a;
  a++;
}