## Slide 1: 15CSE301 Computer Organization and Architecture
Lecture 3
MIPS
Dr Ganesh Neelakanta Iyer
Amrita Vishwa Vidyapeetham, Coimbatore
Associate Professor, Dept of Computer Science and Engg
Reference:
Chapter 2 – 2.1 -2.6, 2.9
Computer Organization and Design, The hardware / software interface, 3rd Edition

## Slide 2: MIPS
Microprocessor without Interlocked Pipeline Stages
It is a reduced instruction set computer (RISC) instruction set architecture (ISA)
Advantages
  Typical of Modern RISC Instruction sets
  Free Simulator Available for Unix, PCs and Macs
  Used in real machines - MIPS R2000 Processors

## Slide 3: MIPS Architecture
32-bit RISC Processor
32 32-bit Registers, $0..$31
Pipelined Execution of Instructions
All instructions are 32-bits
Most Instructions executed in one clock cycle
230 32-bit memory words
Byte addressable memory
  A 32-bit word contains four bytes
  To address the next word of memory add 4

## Slide 4
MIPS Processor
C
P
U
R
e
g
i
s
t
e
r
s
$
0
$
3
1
A
r
i
t
h
m
e
t
i
c
M
u
l
t
i
p
l
y
d
i
v
i
d
e
L
o
H
i
C
o
p
r
o
c
e
s
s
o
r
1
(
F
P
U
)
R
e
g
i
s
t
e
r
s
$
0
$
3
1
A
r
i
t
h
m
e
t
i
c
u
n
i
t
R
e
g
i
s
t
e
r
s
B
a
d
V
A
d
d
r
C
o
p
r
o
c
e
s
s
o
r
0
(
t
r
a
p
s
a
n
d
m
e
m
o
r
y
)
S
t
a
t
u
s
C
a
u
s
e
E
P
C
M
e
m
o
r
y
Prog. Counter
Logic unit
Control
https://web.cse.ohio-state.edu/~crawfis.3/cse675-02/index.html

## Slide 5: MIPS Registers
CPU:
– five control registers;
32-bit program counter – PC;
two 32-bit registers – Hi & Lo, hold results of integer
multiply and divide
– 32 32-bit general purpose registers – GPRs (r0 – r31);
Floating Point Processor – FPU (Coprocessor 1 – CP1):
– 32 32-bit floating point registers – FPRs (f0 – f31);
r0 has fixed value of zero. Attempt to writing into r0 is not
illegal, but its value will not change;
https://web.cse.ohio-state.edu/~crawfis.3/cse675-02/index.html

## Slide 6: MIPS Registers (continued)
Coprocessor 0 (CP0) registers (partial list):
– Status register (CP0reg12) – processor status and control;
– Cause register (CP0reg13) – cause of the most recent
exception;
– EPC register (CP0reg14) – program counter at the last
exception;
BadVAddr register (CP0reg08) – the address for the most
recent address related exception;
Coprocessor 0 – CP0 is incorporated on the MIPS CPU chip
and it provides functions necessary to support operating
system: exception handling, memory management scheduling
and control of critical resources.
https://web.cse.ohio-state.edu/~crawfis.3/cse675-02/index.html

## Slide 7: MIPS Data Types
MIPS operates on:
– 32-bit (unsigned or 2’s complement) integers,
– 32-bit (single precision floating point) real numbers,
– 64-bit (double precision floating point) real numbers;
bytes and half words loaded into GPRs are either zero or sign
bit expanded to fill the 32 bits;
only 32-bit units can be loaded into FPRs; 32-bit real numbers
are stored in even numbered FPRs.
64-bit real numbers are stored in two consecutive FPRs,
starting with even-numbered register.

## Slide 8: MIPS Registers and Memory
Memory
4GB Max
(Typically 64MB-1GB)
0x00000000
0x00000004
0x00000008
0x0000000C
0x00000010
0x00000014
0x00000018
0x0000001C
0xfffffff4
0xfffffffc
0xfffffffc
PC = 0x0000001C
Registers
32 General Purpose Registers
R0
R1
R2
R30
R31
32 bits

## Slide 9: MIPS registers
MIPS has 32 general-purpose registers and another 32 floating-point registers
Registers all begin with a dollar-symbol ($)
The floating point registers are named $f0, $f1, ..., $f31
The general-purpose registers have both names and numbers
When programming in MIPS assembly, it is usually best to use the register names

## Slide 10: MIPS registers and usage
Zero Register
The zero register ($zero or $0) always contains a value of 0. It is built into the hardware and therefore cannot be modified.
$at Register
The $at (Assembler Temporary) register is used for temporary values within pseudo commands. It is not preserved across function calls
For example, with the (slt $at, $a0, $s2) command, $at is set to one if $a0 is less than $s2, otherwise it is set to zero.
$v Registers
The $v Registers are used for returning values from functions. They are not preserved across function calls.
Argument Registers
The $a registers are used for passing arguments to functions. They are not preserved across function calls
Notes: Slt – set if less than

## Slide 11: MIPS registers and usage
Temporaries
The temporary registers are used by the assembler or assembly language programmer to store intermediate values. They are not preserved across function calls.
Saved Temporaries
Saved Temporary registers are used to store longer lasting values. They are preserved across function calls.
$k Registers
The k registers are reserved for use by the OS kernel. They may change randomly at any time as they are used by interrupt handlers.
Pointer Registers
Global Pointer ($gp) - Usually stores a pointer to the global data area (such that it can be accessed with memory offset addressing).
Stack Pointer ($sp) - Used to store the value of the stack pointer.
Frame Pointer ($fp) - Used to store the value of the frame pointer.
Return Address ($ra) - Stores the return address (the location in the program that a function needs to return to).
All Pointer Registers are preserved across function calls

## Slide 12: MIPS Registers and Usage
Each register can be referred to by number or name.

## Slide 13: MIPS arithmetic
All instructions have 3 operands
Operand order is fixed (destination first) Example: C code: a = b + c MIPS ‘code’: add a, b, c “The natural number of operands for an operation like addition is three…requiring every instruction to have exactly three operands, no more and no less, conforms to the philosophy of keeping the hardware simple”

## Slide 14: MIPS arithmetic
Design Principle: simplicity favors regularity.
Of course this complicates some things... C code: a = b + c + d;
Operands must be registers, only 32 registers provided
Each register contains 32 bits
MIPS code: add a, b, c add a, a, d

## Slide 15: Exercise
Write the MIPS code for
f = (g + h) – (i + j);
add t0,g,h # temporary variable t0 contains g + h
add t1,i,j # temporary variable t1 contains i + j
sub f,t0,t1 # f gets t0 – t1, which is (g + h) – (i + j)

## Slide 16: Registers vs. Memory
Processor
I/O
Control
Datapath
Memory
Input
Output
Arithmetic instructions operands must be registers, — only 32 registers provided
Compiler associates variables with registers
What about programs with lots of variables

## Slide 17: Memory Organization
Viewed as a large, single-dimension array, with an address
A memory address is an index into the array
"Byte addressing" means that the index points to a byte of memory.
0
1
2
3
4
5
6
...
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data

## Slide 18: More about MIPS Memory Organization
Two views of memory:
  232 bytes with addresses 0, 1, 2, …, 232-1
  230 4-byte words* with addresses 0, 4, 8, …, 232-4
Both views use byte addresses
Word address must be multiple of 4 (aligned)
8 bits
0x00000000
0x00000001
0x00000002
0x00000003
0x00000000
0x00000004
0x00000008
0x0000000C
32 bits
0
1
2
3
*Word sizes vary in other architectures
Not all architectures require this

## Slide 19: MIPS Addressing Modes
Register addressing
Indexed Address - Adds address field and register value and uses this as address of operand in memory
  Example 100($2) - Adds 100 to the value in register 2 and reads the operand from the resulting memory address
  Used for array X[I] operations, the array index is normally in the register and the address field is the first location in the array

## Slide 20: MIPS Addressing Modes
Immediate Addressing - Uses constant value contained in instruction
  Example addi $1,$2,4 - adds constant 4 to register 2 and stores result in register 1
  Used for constants in programs
PC relative - Address from instruction is added to the current value in the Program Counter
  Example J 4 - Jumps to address PC+4
  Saves address bits in jump instructions

## Slide 21: MIPS Alignment
MIPS restricts memory accesses to be aligned as follows:
– 32-bit word has to start at byte address that is multiple of 4;
32-bit word at address 4n includes four bytes with addresses
4n, 4n+1, 4n+2, and 4n+3
– 16-bit half word has to start at byte address that is multiple of 2;
16-bit word at address 2n includes two bytes with addresses
2n and 2n+1.

## Slide 22: MIPS Instructions
32-bit fixed format instruction and 3 formats;
register – register and register-immediate computational
instructions;
single address mode for load/store instructions: – register content + offset (called base addressing);
simple branch conditions;
  – branch instructions use PC relative addressing;
  – branch address = [PC] + 4 + 4×offset
jump instructions with:
  – 28-bit addresses (jumps inside 256 megabyte regions),
  or
  – absolute 32-bit addresses.

## Slide 23: MIPS Instructions
Instructions that move data:
  load to register from memory,
  store from register to memory,
  move between registers in same and different coprocessors
ALU integer instructions,
Floating point instructions,
Control-related instructions,
Special control-related instructions.

## Slide 24
MIPS Instructions

## Slide 25: MIPS Instructions
All instructions exactly 32 bits wide
Different formats for different purposes
Similarities in formats ease implementation
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format
31
0
31
0
31
0

## Slide 26: MIPS Arithmetic
All MIPS arithmetic instructions have 3 operands
Operand order is fixed (e.g., destination first)
Example: C code: A = B + C MIPS code: add $s0, $s1, $s2
compiler’s job to associate variables with registers

## Slide 27: MIPS Arithmetic
Design Principle 1: simplicity favors regularity.
Translation: Regular instructions make for simple hardware!
Simpler hardware reduces design time and manufacturing cost.
Of course this complicates some things... C code: A = B + C + D; E = F - A; MIPS code add $t0, $s1, $s2 (arithmetic): add $s0, $t0, $s3 sub $s4, $s5, $s0
Performance penalty: high-level code translates to denser machine code.
Allowing variable number
of operands would
simplify the assembly
code but complicate the
hardware.

## Slide 28: MIPS Arithmetic
Operands must be in registers – only 32 registers provided (which require 5 bits to select one register). Reason for small number of registers:
Design Principle 2: smaller is faster. Why?
  Electronic signals have to travel further on a physically larger chip increasing clock cycle time.
  Smaller is also cheaper!

## Slide 29: MIPS Instructions R Instructions
R instructions are used when all the data values used by the instruction are located in registers
All R-type instructions have the following format:
OP rd, rs, rt
Where "OP" is the mnemonic for the particular instruction. rs, and rt are the source registers, and rd is the destination register. As an example, the add mnemonic can be used as:
add $s1, $s2, $s3
Where the values in $s2 and $s3 are added and the result is stored in $s1

## Slide 30: MIPS Instructions R Format
Converting an R mnemonic into the equivalent binary machine code is performed in the following way:
opcode | rs | rt | rd | shift (shamt) | funct
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
Opcode
  The opcode is the machine code representation of the instruction mnemonic. The opcode field is 6 bits long (bit 26 to bit 31)
rs, rt, rd
  The numeric representations of the source registers and the destination register. These numbers correspond to the $X representation of a register, such as $0 or $31. Each of these fields is 5 bits long. (25 to 21, 20 to 16, and 15 to 11, respectively)
Shift (shamt)
  Used with the shift and rotate instructions, this is the amount by which the source operand rs is rotated/shifted. This field is 5 bits long (6 to 10)
Funct
  For instructions that share an opcode, the funct parameter contains the necessary control codes to differentiate the different instructions. 6 bits long (0 to 5). Example: Opcode 0x00 accesses the ALU, and the funct selects which ALU function to use

## Slide 31: Arithmetic & Logical Instructions - Binary Representation
Used for arithmetic, logical, shift instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  rd: register destination operand
  shamt: shift amount
  funct: function - specific type of operation
Also called “R-Format” or “R-Type” Instructions
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
0
31

## Slide 32: Arithmetic & Logical Instructions - Binary Representation Example
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
Decimal
Binary
Machine language for add $8, $17, $18
See reference card for op, funct values
000000
0
10001
17
10010
18
01000
8
00000
0
100000
32
0
31

## Slide 33: MIPS Data Transfer Instructions
Transfer data between registers and memory
Instruction format (assembly) lw $dest, offset($addr) load word sw $src, offset($addr) store word
Uses:
  Accessing a variable in main memory
  Accessing an array element

## Slide 34: Example - Loading a Simple Variable
lw R5,8(R2)
Memory
0x00
Variable Z = 692310
Variable X
Variable Y
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
8
+
Registers
R0=0 (constant)
R1
R2=0x10
R30
R31
R3
R4
R5
R5
R2=0x10
R5 = 629310
Variable Z = 692310

## Slide 35: Data Transfer Example - Array Variable
Registers
R0=0 (constant)
R1
R2=0x08
R30
R31
R3
R4
R5=105
C Program: int a[5];
a[3] = z;
Assembly: sw $5,12($2)
12=0xc
+
Memory
0x00
a[0]
a[4]
a[2]
a[1]
a[3]
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
Base Address
R5=105
R2=0x08
a[3]=105
scaled offset

## Slide 36: MIPS Instructions I instructions
I instructions are used when the instruction must operate on an immediate value and a register value
Immediate values may be a maximum of 16 bits long
Larger numbers may not be manipulated by immediate instructions
I instructions are called in the following way:
OP rt, IMM(rs)
However, beq and bne instructions are called in the following way:
OP rs, rt, IMM
Where rt is the target register, rs is the source register, and IMM is the immediate value. The immediate value can be up to 16 bits long
For instance, the addi instruction can be called as:
addi $s1, $s2, 100
Where the value of $s2 plus 100 is stored in $s1

## Slide 37: MIPS Instructions I Format
I instructions are converted into machine code words in the following format:
opcode | rs | rt | IMM
6 bits | 5 bits | 5 bits | 16 bits
Opcode
  The 6-bit opcode of the instruction
  In I instructions, all mnemonics have a one-to-one correspondence with the underlying opcodes
  This is because there is no funct parameter to differentiate instructions with an identical opcode. 6 bits (26 to 31)
rs, rt
  The source and target register operands, respectively
  5 bits each (21 to 25 and 16 to 20, respectively)
IMM
  The 16 bit immediate value. 16 bits (0 to 15)
  This value is usually used as the offset value in various instructions, and depending on the instruction, may be expressed in two's complement.

## Slide 38: Data Transfer Instructions - Binary Representation
Used for load, store instructions
  op: Basic operation of the instruction (opcode)
  rs: first register source operand
  rt: second register source operand
  offset: 16-bit signed address offset (-32,768 to +32,767)
Also called “I-Format” or “I-Type” instructions
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Address

## Slide 39: I-Format vs. R-Format Instructions
Compare with R-Format
offset
6 bits
5 bits
5 bits
16 bits
I-Format
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
op
rs
rt
Note similarity!

## Slide 40: I-Format Example
Machine language for lw $9, 1200($8) == lw $t1, 1200($t0)
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Binary
Decimal
35
8
9
1200
100011
01000
01001
0000010010110000
0
31

## Slide 41: MIPS Instructions J instructions
J instructions are used when a jump needs to be performed
The J instruction has the most space for an immediate value, because addresses are large numbers
J instructions are called in the following way
OP LABEL
Where OP is the mnemonic for the particular jump instruction, and LABEL is the target address to jump to

## Slide 42: MIPS Instructions J Format
J instructions have the following machine-code format:
opcode | Pseudo-Address
6 bits | 26 bits
Opcode
  The 6 bit opcode corresponding to the particular jump command. (26 to 31)
Address
  A 26-bit shortened address of the destination. (0 to 25)
  The two least significant bits are removed, and the 4 most significant bits are removed, and assumed to be the same as the current instruction's address

## Slide 43: MIPS Instruction Types
Arithmetic & Logical - manipulate data in registers add $s1, $s2, $s3 $s1 = $s2 + $s3 or $s3, $s4, $s5 $s3 = $s4 OR $s5
Data Transfer - move register data to/from memory lw $s1, 100($s2) $s1 = Memory[$s2 + 100] sw $s1, 100($s2) Memory[$s2 + 100] = $s1
Branch - alter program flow beq $s1, $s2, 25 if ($s1==$s1) PC = PC + 4 + 4*25

## Slide 44: MIPS Assembly Language Examples
ADD $1,$2,$3
  Register 1 = Register 2 + Register 3
SUB $1,$2,$3
  Register 1 = Register 2 - Register 3
AND $1,$2,$3
  Register 1 = Register 2 AND Register 3
ADDI $1,$2,10
  Register 1 = Register 2 + 10
SLL $1, $2, 10
  Register 1 = Register 2 shifted left 10 bits

## Slide 45: MIPS Assembly Language Examples
LW $1,100
  Register 1 = Contents of memory location 100
  Used to load registers
SW $1,100
  Contents of memory location 100 = Register 1
  Used to save registers
LUI $1,100
  Register 1 upper 16-bits = 100
  Lower 16-bits are set to all 0’s
  Used to load a constant in the upper 16-bits
  Other constants in instructions are only 16-bits, so this instruction is used when a constant larger than 16-bits is required for the operation

## Slide 46: MIPS Assembly Language Examples
J 100
  Jumps to PC+100
JAL 100
  Save PC in $31 and Jumps to PC+100
  Used for subroutine calls
JR $31
  Jumps to address in register 31
  Used for subroutine returns

## Slide 47: MIPS Assembly Language Examples
BEQ $1, $2, 100
  If register 1 equal to register 2 jump to PC+100
  Used for Assembly Language If statements
BNE $1, $2, 100
  If register 1 not equal to register 2 jump to PC+100
  Used for Assembly Language If statements

## Slide 48: MIPS Assembly Language Examples
SLT $1,$2,$3
  If register 2 is less than register 3 then register 1=1 else register 1=0
  In an assembly language flag a “1” means true and a “0” means false
  Used in conjunction with Bxx instruction to implement any arithmetic comparision
  Required for more complex assembly language If statements

## Slide 49: MIPS Arithmetic & Logical Instructions
Instruction usage (assembly) add dest, src1, src2 dest=src1 + src2 sub dest, src1, src2 dest=src1 - src2 and dest, src1, src2 dest=src1 AND src2
Instruction characteristics
  Always 3 operands: destination + 2 sources
  Operand order is fixed
  Operands are always general purpose registers
Design Principles:
  Design Principle 1: Simplicity favors regularity
  Design Principle 2: Smaller is faster

## Slide 50: MIPS Conditional Branch Instructions
Conditional branches allow decision making
beq R1, R2, LABEL if R1==R2 goto LABEL bne R3, R4, LABEL if R3!=R4 goto LABEL
Example
C Code if (i==j) goto L1; f = g + h; L1: f = f - i; Assembly beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3

## Slide 51: Example: Compiling C if-then-else
Example C Code if (i==j) f = g + h; else f = g - h; Assembly bne $s3, $s4, Else add $s0, $s1, $s2 j Exit; # new: unconditional jump Else: sub $s0, $s0, $s3 Exit:
New Instruction: Unconditional jump j LABEL # goto Label

## Slide 52: Binary Representation - Branch
Branch instructions use I-Format
offset is added to PC when branch is taken beq r0, r1, offset has the effect: if (r0==r1) pc = pc + 4 + (offset << 2) else pc = pc + 4;
Offset is specified in instruction words (why?)
What is the range of the branch target addresses?
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Conversion to
word offset

## Slide 53: Branch Example
Machine language for beq $s3, $s4, L1 add $s0, $s1, $s2 L1: sub $s0, $s0, $s3
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
Binary
Decimal
4
19
20
1
000100
10011
10100
0000000000000001
$19
$20
PC
PC+4
Target
of beq
1-instruction
offset
0
31

## Slide 54: Comparisons - What about <, <=, >, >=?
bne, beq provide equality comparison
slt provides magnitude comparison slt $t0,$s3,$s4 # if $s3<$s4 $t0=1; # else $t0=0;
Combine with bne or beq to branch: slt $t0,$s3,$s4 # if (a<b) bne $t0,$zero, Less # goto Less;
Why not include a blt instruction in hardware?
  Supporting in hardware would lower performance
  Assembler provides this function if desired (by generating the two instructions)
condition register

## Slide 55: Binary Representation - Jump
Jump Instruction uses J-Format (op=2)
What happens during execution? PC = PC[31:28] : (IR[25:0] << 2)
op
address
6 bits
26 bits
Conversion to word offset
Concatenate upper 4 bits of PC to form complete 32-bit address

## Slide 56: Jump Example
Machine language for j L5
Assume L5 is at address 0x00400020
and
PC <= 0x03FFFFFF
Binary
Decimal/Hex
op
address
6 bits
26 bits
2
0x0100008
000010
00000100000000000000001000
>>2
lower 28
bits
0x0100008
31
0

## Slide 57: Constants / Immediate Instructions
Small constants are used quite frequently (50% of operands) e.g., A = A + 5; B = B + 1; C = C - 18;
MIPS Immediate Instructions (I-Format): addi $29, $29, 4 slti $8, $18, 10 andi $29, $29, 6 ori $29, $29, 4
Allows up to 16-bit constants
How do you load just a constant into a register?
ori $5, $zero, 666
Arithmetic instructions sign-extend immed.
Logical instructions don’t sign extend immed.

## Slide 58: Why are Immediates only 16 bits?
Because 16 bits fits neatly in a 32-bit instruction
Because most constants are small (i.e. < 16 bits)
Design Principle 3: Make the Common Case Fast

## Slide 59: MIPS Logical Instructions
and, andi - bitwise AND
or, ori - bitwise OR
Example
and $s2,$s0,$s1
ori $s3,s2,252
11011111010110100100100011110101
11110000111100001111000011110000
$s0
$s1
$s2
11010000010100000100000011110000
$s3
11010000010100000100000011111100
00000000000000000000000011111100
(25210)

## Slide 60: 32-Bit Immediates and Address
(original contents)
$t0
Immediate operations provide for 16-bit constants.
What about when we need larger constants?
Use "load upper immediate - lui” (I-Format) to set the upper 16 bits of a constant in a register.
lui $t0, 1010101010101010
Then use ori to fill in lower 16 bits: ori $t0, $t0, 1010101010101010
1010101010101010
0000000000000000
filled with zeros
$t0
1010101010101010
0000000000000000
1010101010101010

## Slide 61: MIPS Shift Instructions
MIPS Logical Shift Instructions
  Shift left: sll (shift-left logical) instruction
  Right shift: srl (shift-right logical) instruction
sll $s1,$s0,8
srl $s2,$s1,4
01011010010010001111010100000000
Zeros shift in
00000101101001001000111101010000
Zeros shift in
11011111010110100100100011110101
$s0
$s1
$s2

## Slide 62: Shift Instruction Encodings
Applications
  Bitfield access (see book)
  Multiplication / Division by power of 2
  Example: array access sll $t0,$t1,2 # $t0=$t1*4 add $t3,$t1,$t2 lw $t3, 0($t3)
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
srl
0
rs
rt
rd
0
shamt
sll
0
rs
rt
rd
6
shamt
unused

## Slide 63: How to Decode?
What is the assembly language statement corresponding to this machine instruction?
0x00af8020
Convert to binary
  0000 0000 1010 1111 1000 0000 0010 0000
Decode
  op: 00000
  rs: 00101
  rt: 01111
  rd: 10000
  shamt: 00000
  funct: 100000
Solution: add $s0, $a1, $t7

## Slide 64: Compromise in MIPS
Design Principle 4: Good design demands good compromises
The compromise chosen by the MIPS designers is to keep all instructions the same length, thereby requiring different kinds of instruction formats for different kinds of instructions

## Slide 65
MIPS - Summary

## Slide 66: Summary - MIPS Instruction Set
simple instructions all 32 bits wide
very structured, no unnecessary baggage
only three instruction formats
op
rs
rt
offset
6 bits
5 bits
5 bits
16 bits
op
rs
rt
rd
funct
shamt
6 bits
5 bits
5 bits
5 bits
5 bits
6 bits
R-Format
I-Format
op
address
6 bits
26 bits
J-Format

## Slide 67: MIPS addressing modes
Immediate addressing
Register addressing
Base or displacement addressing
PC-relative addressing
Pseudodirect addressing,
where the operand is a constant within the instruction itself
where the operand is a register
where the operand is at the memory location whose address is the sum of a register and a constant in the instruction
where the branch address is the sum of the PC and a constant in the instruction
where the jump address is the 26 bits of the instruction concatenated with the upper bits of the PC

## Slide 68: MIPS design principles in a nut shell
Simplicity favors regularity
Fixed size instructions, 3 register operands in every arithmetic operation, keeping the register fields at the same place in every instruction format
Smaller is faster
MIPS has 32 32-bit registers,$v0,...$v31, a very large number would increase the clock cycle time.
Good design demands compromise.
The compromise represented by the MIPS design, was to make all the instructions the same length, thereby requiring different instruction formats.
Make the common case fast.
The MIPS instruction set addresses this principal by making constants part of arithmetic instructions. Furthermore, by loading small constants into the upper 16-bits of a register.

## Slide 69: MIPS Instructions

## Slide 70
Office Hours
  Monday 1120-1210 @ My office