## Slide 1: 15CSE301 Computer Organization and Architecture
Pipelining
Dr Ganesh Neelakanta Iyer
Amrita Vishwa Vidyapeetham, Coimbatore
Associate Professor, Dept of Computer Science and Engg
Reference:
Chapter 6
Computer Organization and Design, The hardware / software interface, 3rd Edition

## Slide 2: Overview
Pipelining is widely used in modern processors.
Pipelining improves system performance in terms of throughput.
Pipelined organization requires sophisticated compilation techniques.

## Slide 3: Basic Concepts

## Slide 4: Making the Execution of Programs Faster
Use faster circuit technology to build the processor and the main memory.
Arrange the hardware so that more than one operation can be performed at the same time.
In the latter way, the number of operations performed per second is increased even though the elapsed time needed to perform any one operation is not changed.

## Slide 5: Traditional Pipeline Concept
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 6: Traditional Pipeline Concept
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 7: Traditional Pipeline Concept
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 8: Traditional Pipeline Concept
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Unbalanced lengths of pipe stages reduces speedup
Time to “fill” pipeline and time to “drain” it reduces speedup
Stall for Dependences
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 9: Use the Idea of Pipelining in a Computer
F
1
E
1
F
2
E
2
F
3
E
3
I
1
I
2
I
3
(a) Sequential execution
Instruction
fetch
unit
Ex
ecution
unit
Interstage buffer
B1
(b) Hardware organization
T
ime
F
1
E
1
F
2
E
2
F
3
E
3
I
1
I
2
I
3
Instruction
(c) Pipelined execution
Basic idea of instruction pipelining.
Clock cycle
1
2
3
4
T
ime
Fetch + Execution

## Slide 10: Use the Idea of Pipelining in a Computer
Fetch + Decode
+ Execution + Write

## Slide 11: Characteristics Of Pipelining
If the stages of a pipeline are not balanced and one stage is slower than another, the entire throughput of the pipeline is affected.
In terms of a pipeline within a CPU, each instruction is broken up into different stages. Ideally if each stage is balanced (all stages are ready to start at the same time and take an equal amount of time to execute.) the time taken per instruction (pipelined) is defined as: Time per instruction (unpipelined) / Number of stages

## Slide 12: Problem
Consider a pipeline having 4 phases with duration 60, 50, 90 and 80 ns. Given latch delay is 10 ns. Calculate-
  Pipeline cycle time
  Non-pipeline execution time
  Speed up ratio
  Pipeline time for 1000 tasks
  Sequential time for 1000 tasks
  Throughput

## Slide 13: Answer
Part-01: Pipeline Cycle Time-
Cycle time
= Maximum delay due to any stage + Delay due to its register
= Max { 60, 50, 90, 80 } + 10 ns
90+10 = 100 ns

## Slide 14: Answer
Part-02: Non-Pipeline Execution Time-
Non-pipeline execution time for one instruction
= 60 ns + 50 ns + 90 ns + 80 ns
= 280 ns

## Slide 15: Answer
Part-03: Speed Up Ratio-
Speed up
= Non-pipeline execution time / Pipeline execution time
= 280 ns / Cycle time
= 280 ns / 100 ns
= 2.8

## Slide 16: Answer
Part-04: Pipeline Time For 1000 Tasks-
Pipeline time for 1000 tasks
= Time taken for 1st task + Time taken for remaining 999 tasks
= 1 x 4 clock cycles + 999 x 1 clock cycle
= 4 x cycle time + 999 x cycle time
= 4 x 100 ns + 999 x 100 ns
= 400 ns + 99900 ns
= 100300 ns

## Slide 17: Answer
Part-05: Sequential Time For 1000 Tasks-
Non-pipeline time for 1000 tasks
= 1000 x Time taken for one task
= 1000 x 280 ns
= 280000 ns

## Slide 18: Answer
Part-06: Throughput-
Throughput for pipelined execution
= Number of instructions executed per unit time
= 1000 tasks / 100300 ns

## Slide 19: More problems
https://www.gatevidyalay.com/pipelining-practice-problems/

## Slide 20: Characteristics Of Pipelining
The previous expression is ideal. We will see later that there are many ways in which a pipeline cannot function in a perfectly balanced fashion.
In terms of a CPU, the implementation of pipelining has the effect of reducing the average instruction time, therefore reducing the average CPI.
EX: If each instruction in a microprocessor takes 5 clock cycles (unpipelined) and we have a 4 stage pipeline, the ideal average CPI with the pipeline will be 1.25 .

## Slide 21: RISC Instruction Set Implementation
We first need to look at how instructions in the MIPS64 instruction set are implemented without pipelining. We’ll assume that any instruction of the subset of MIPS64 can be executed in at most 5 clock cycles.
The five clock cycles will be broken up into the following steps:
    Instruction Fetch Cycle
    Instruction Decode/Register Fetch Cycle
    Execution Cycle
    Memory Access Cycle
    Write-Back Cycle

## Slide 22: Looking At The Big Picture
Overall the most time that an non-pipelined instruction can take is 5 clock cycles. Below is a summary:
    Branch - 2 clock cycles
    Store - 4 clock cycles
    Other - 5 clock cycles
EX: Assuming branch instructions account for 12% of all instructions and stores account for 10%, what is the average CPI of a non-pipelined CPU?
ANS: 0.12*2+0.10*4+0.78*5
= 4.54

## Slide 23: The Classical RISC 5 Stage Pipeline
In an ideal case to implement a pipeline we just need to start a new instruction at each clock cycle.
Unfortunately there are many problems with trying to implement this
  Obviously we cannot have the ALU performing an ADD operation and a MULTIPLY at the same time
  But if we look at each stage of instruction execution as being independent, we can see how instructions can be “overlapped”.

## Slide 24: Instruction execution review
Executing a MIPS instruction can take up to five steps.
However, as we saw, not all instructions need all five steps.
Step | Name | Description
Instruction Fetch | IF | Read an instruction from memory.
Instruction Decode | ID | Read source registers and generate control signals.
Execute | EX | Compute an R-type result or a branch outcome.
Memory | MEM | Read or write the data memory.
Writeback | WB | Store a result in the destination register.
Instruction | Steps required |  |  |  | 
beq | IF | ID | EX |  | 
R-type | IF | ID | EX |  | WB
sw | IF | ID | EX | MEM | 
lw | IF | ID | EX | MEM | WB

## Slide 25: Example: Instruction Fetch (IF)
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Let’s quickly review how lw is executed in the single-cycle datapath.
We’ll ignore PC incrementing and branching for now.
In the Instruction Fetch (IF) step, we read the instruction memory.

## Slide 26: Instruction Decode (ID)
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
The Instruction Decode (ID) step reads the source register from the register file.

## Slide 27: Execute (EX)
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
The third step, Execute (EX), computes the effective memory address from the source register and the instruction’s constant field.

## Slide 28: Memory (MEM)
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
The Memory (MEM) step involves reading the data memory, from the address computed by the ALU.

## Slide 29: Writeback (WB)
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Finally, in the Writeback (WB) step, the memory value is stored into the destination register.

## Slide 30: A bunch of lazy functional units
Notice that each execution step uses a different functional unit.
In other words, the main units are idle for most of the 8ns cycle!
  The instruction RAM is used for just 2ns at the start of the cycle.
  Registers are read once in ID (1ns), and written once in WB (1ns).
  The ALU is used for 2ns near the middle of the cycle.
  Reading the data memory only takes 2ns as well.
That’s a lot of hardware sitting around doing nothing.

## Slide 31: Putting those slackers to work
We shouldn’t have to wait for the entire instruction to complete before we can re-use the functional units.
For example, the instruction memory is free in the Instruction Decode step as shown below, so...
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Instruction Decode (ID)
Idle

## Slide 32: Decoding and fetching together
Why don’t we go ahead and fetch the next instruction while we’re decoding the first one?
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Read
address
Decode 1st instruction
Fetch 2nd

## Slide 33: Executing, decoding and fetching
Similarly, once the first instruction enters its Execute stage, we can go ahead and decode the second instruction.
But now the instruction memory is free again, so we can fetch the third instruction!
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
Decode 2nd
Fetch 3rd
Execute 1st

## Slide 34: Making Pipelining Work
We’ll make our pipeline 5 stages long, to handle load instructions as they were handled in the multi-cycle implementation
  Stages are: IF, ID, EX, MEM, and WB
We want to support executing 5 instructions simultaneously: one in each stage.

## Slide 35: Break datapath into 5 stages
Each stage has its own functional units.
Each stage can execute in 2ns
  Just like the multi-cycle implementation
Read
address
Instruction
memory
Instruction
[31-0]
Read
address
Write
address
Write
data
Data
memory
Read
data
MemWrite
MemRead
1
M
u
x
0
MemToReg
Sign
extend
0
M
u
x
1
ALUSrc
Result
Zero
ALU
ALUOp
I [15 - 0]
I [25 - 21]
I [20 - 16]
I [15 - 11]
0
M
u
x
1
RegDst
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 2
Read
data 1
Registers
RegWrite
ID
IF
EXE
MEM
WB
2ns
2ns
2ns
2ns

## Slide 36: Pipelining Loads
6 PM
7
8
9
Time
30
40
40
40
40
20
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
lw $t1, 8($sp) |  | IF | ID | EX | MEM | WB |  |  | 
lw $t2, 12($sp) |  |  | IF | ID | EX | MEM | WB |  | 
lw $t3, 16($sp) |  |  |  | IF | ID | EX | MEM | WB | 
lw $t4, 20($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 37: A pipeline diagram
A pipeline diagram shows the execution of a series of instructions.
  The instruction sequence is shown vertically, from top to bottom.
  Clock cycles are shown horizontally, from left to right.
  Each instruction is divided into its component stages. (We show five stages for every instruction, which will make the control unit easier.)
This clearly indicates the overlapping of instructions. For example, there are three instructions active in the third cycle above.
  The “lw” instruction is in its Execute stage.
  Simultaneously, the “sub” is in its Instruction Decode stage.
  Also, the “and” instruction is just being fetched.
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | MEM | WB |  |  | 
and $t1, $t2, $t3 |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | MEM | WB | 
add $sp, $sp, -4 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 38: Pipeline terminology
The pipeline depth is the number of stages—in this case, five.
In the first four cycles here, the pipeline is filling, since there are unused functional units.
In cycle 5, the pipeline is full. Five instructions are being executed simultaneously, so all hardware units are in use.
In cycles 6-9, the pipeline is emptying.
filling
full
emptying
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | MEM | WB |  |  | 
and $t1, $t2, $t3 |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | MEM | WB | 
add $sp, $sp, -4 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 39: Pipelining Performance
Execution time on ideal pipeline:
  time to fill the pipeline + one cycle per instruction
  What is the execution time for N instructions?
Compare with other implementations:
  Single Cycle: (8ns clock period)
How much faster is pipelining for N=1000 ?
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
lw $t1, 8($sp) |  | IF | ID | EX | MEM | WB |  |  | 
lw $t2, 12($sp) |  |  | IF | ID | EX | MEM | WB |  | 
lw $t3, 16($sp) |  |  |  | IF | ID | EX | MEM | WB | 
lw $t4, 20($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 40: Pipeline Datapath: Resource Requirements
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
lw $t0, 4($sp) | IF | ID | EX | MEM | WB |  |  |  | 
lw $t1, 8($sp) |  | IF | ID | EX | MEM | WB |  |  | 
lw $t2, 12($sp) |  |  | IF | ID | EX | MEM | WB |  | 
lw $t3, 16($sp) |  |  |  | IF | ID | EX | MEM | WB | 
lw $t4, 20($sp) |  |  |  |  | IF | ID | EX | MEM | WB
We need to perform several operations in the same cycle.
  Increment the PC and add registers at the same time.
  Fetch one instruction while another one reads or writes data.
What does this mean for our hardware?

## Slide 41: Pipelining other instruction types
R-type instructions only require 4 stages: IF, ID, EX, and WB
  We don’t need the MEM stage
What happens if we try to pipeline loads with R-type instructions?
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | WB |  |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | WB |  |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | WB |  | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 42: Important Observation
Each functional unit can only be used once per instruction
Each functional unit must be used at the same stage for all instructions. See the problem if:
  Load uses Register File’s Write Port during its 5th stage
  R-type uses Register File’s Write Port during its 4th stage
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | WB |  |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | WB |  |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | WB |  | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 43: A solution: Insert NOP stages
Enforce uniformity
  Make all instructions take 5 cycles.
  Make them have the same stages, in the same order
    Some stages will do nothing for some instructions
    Stores and Branches have NOP stages, too…
 | Clock cycle |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
add $sp, $sp, -4 | IF | ID | EX | NOP | WB |  |  |  | 
sub $v0, $a0, $a1 |  | IF | ID | EX | NOP | WB |  |  | 
lw $t0, 4($sp) |  |  | IF | ID | EX | MEM | WB |  | 
or $s0, $s1, $s2 |  |  |  | IF | ID | EX | NOP | WB | 
lw $t1, 8($sp) |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 44: Summary
Pipelining attempts to maximize instruction throughput by overlapping the execution of multiple instructions.
Pipelining offers amazing speedup.
  In the best case, one instruction finishes on every cycle, and the speedup is equal to the pipeline depth.
The pipeline datapath is much like the single-cycle one, but with added pipeline registers
  Each stage needs is own functional units
Next time we’ll see the datapath and control, and walk through an example execution.

## Slide 45: Pipeline: Hazards
Portions of these slides are derived from:
Dave Patterson © UCB

## Slide 46: Pipeline Hazards
Where one instruction cannot immediately follow another
Types of hazards
  Structural hazards - attempt to use the same resource by two or more instructions
  Control hazards - attempt to make branching decisions before branch condition is evaluated
  Data hazards - attempt to use data before it is ready
Can always resolve hazards by waiting

## Slide 47: Structural Hazards
Attempt to use the same resource by two or more instructions at the same time
Example: Single Memory for instructions and data
  Accessed by IF stage
  Accessed at same time by MEM stage
Solutions
  Delay the second access by one clock cycle, OR
  Provide separate memories for instructions & data
    This is what the book does
    This is called a “Harvard Architecture”
    Real pipelined processors have separate caches

## Slide 48: Pipelined Example - Executing Multiple Instructions
Consider the following instruction sequence:
    lw $r0, 10($r1)
    sw $sr3, 20($r4)
    add $r5, $r6, $r7
    sub $r8, $r9, $r10

## Slide 49: Executing Multiple Instructions Clock Cycle 1
LW

## Slide 50: Executing Multiple Instructions Clock Cycle 2
LW
SW

## Slide 51: Executing Multiple Instructions Clock Cycle 3
LW
SW
ADD

## Slide 52: Executing Multiple Instructions Clock Cycle 4
LW
SW
ADD
SUB

## Slide 53: Executing Multiple Instructions Clock Cycle 5
LW
SW
ADD
SUB

## Slide 54: Executing Multiple Instructions Clock Cycle 6
SW
ADD
SUB

## Slide 55: Executing Multiple Instructions Clock Cycle 7
ADD
SUB

## Slide 56: Executing Multiple Instructions Clock Cycle 8
SUB

## Slide 57: Alternative View - Multicycle Diagram

## Slide 58: Alternative View - Multicycle Diagram
Memory Conflict

## Slide 59: One Memory Port Structural Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 60: Structural Hazards
Some common Structural Hazards:
Memory:
  we’ve already mentioned this one.
Floating point:
  Since many floating point instructions require many cycles, it’s easy for them to interfere with each other.
Starting up more of one type of instruction than there are resources.
  For instance, the PA-8600 can support two ALU + two load/store instructions per cycle - that’s how much hardware it has available.

## Slide 61: Structural Hazards
Dealing with Structural Hazards
Stall
low cost, simple
Increases CPI
use for rare case since stalling has performance effect
Pipeline hardware resource
useful for multi-cycle resources
good performance
sometimes complex e.g., RAM
Replicate resource
good performance
increases cost (+ maybe interconnect delay)
useful for cheap or divisible resources

## Slide 62: Structural Hazards
Structural hazards are reduced with these rules:
  Each instruction uses a resource at most once
  Always use the resource in the same pipeline stage
  Use the resource for one cycle only
Many RISC ISAs are designed with this in mind
Sometimes very difficult to do this.
  For example, memory of necessity is used in the IF and MEM stages.

## Slide 63: Structural Hazards
We want to compare the performance of two machines. Which machine is faster?
Machine A: Dual ported memory - so there are no memory stalls
Machine B: Single ported memory, but its pipelined implementation has a clock rate that is 1.05 times faster
Assume:
Ideal CPI = 1 for both
Loads are 40% of instructions executed

## Slide 64: Speed Up Equations for Pipelining
For simple RISC pipeline, CPI = 1:

## Slide 65: Structural Hazards
We want to compare the performance of two machines. Which machine is faster?
Machine A: Dual ported memory - so there are no memory stalls
Machine B: Single ported memory, but its pipelined implementation has a 1.05 times faster clock rate
Assume:
Ideal CPI = 1 for both
Loads are 40% of instructions executed
SpeedUpA = Pipeline Depth/(1 + 0) x (clockunpipe/clockpipe)
= Pipeline Depth
SpeedUpB = Pipeline Depth/(1 + 0.4 x 1) x (clockunpipe/(clockunpipe / 1.05)
= (Pipeline Depth/1.4) x 1.05
= 0.75 x Pipeline Depth
SpeedUpA / SpeedUpB = Pipeline Depth / (0.75 x Pipeline Depth) = 1.33
Machine A is 1.33 times faster

## Slide 66: Pipelining Summary
Speed Up <= Pipeline Depth; if ideal CPI is 1, then:
Hazards limit performance on computers:
  Structural: need more HW resources
  Data (RAW,WAR,WAW)
  Control
Speedup =
Pipeline Depth
1 + Pipeline stall CPI
X
Clock Cycle Unpipelined
Clock Cycle Pipelined

## Slide 67: Review
Speedup =
Pipeline Depth
1 + Pipeline stall CPI
X
Clock Cycle Unpipelined
Clock Cycle Pipelined
Speedup of pipeline

## Slide 68: Data Hazards
Data hazards occur when data is used before it is ready
The use of the result of the SUB instruction in the next three instructions causes a data hazard, since the register $2 is not written until after those instructions read it.

## Slide 69: Data Hazards
Read After Write (RAW)
InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
Execution Order is:
InstrI
InstrJ
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 70: Data Hazards
Write After Read (WAR)
InstrJ tries to write operand before InstrI reads i
  Gets wrong operand
  Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
Execution Order is:
InstrI
InstrJ
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 71: Data Hazards
Write After Write (WAW)
InstrJ tries to write operand before InstrI writes it
  Leaves wrong result ( InstrI not InstrJ )
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW later in more complicated pipes
Execution Order is:
InstrI
InstrJ
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 72: Data Hazard Detection in MIPS (1)
IF/ID
ID/EX
EX/MEM
MEM/WB
Read after Write
1a: EX/MEM.RegisterRd = ID/EX.RegisterRs
1b: EX/MEM.RegisterRd = ID/EX.RegisterRt
2a: MEM/WB.RegisterRd = ID/EX.RegisterRs
2b: MEM/WB.RegisterRd = ID/EX.RegisterRt
EX hazard
MEM hazard

## Slide 73: Data Hazards
Solutions for Data Hazards
  Stalling
  Forwarding:
    connect new value directly to next stage
  Reordering

## Slide 74: Data Hazard - Stalling

## Slide 75: Data Hazards - Stalling
Simple Solution to RAW
Hardware detects RAW and stalls
Assumes register written then read each cycle
  + low cost to implement, simple
  -- reduces IPC
Try to minimize stalls
Minimizing RAW stalls
Bypass/forward/short­circuit (We will use the word “forward”)
Use data before it is in the register
  + reduces/avoids stalls
  -- complex
Crucial for common RAW hazards

## Slide 76: Data Hazards - Forwarding
Key idea: connect new value directly to next stage
Still read s0, but ignore in favor of new result
Problem: what about load instructions?

## Slide 77: Data Hazards - Forwarding
STALL still required for load - data avail. after MEM
MIPS architecture calls this delayed load, initial implementations required compiler to deal with this

## Slide 78: Data Hazards
This is another representation of the stall.
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  | 
SUB R4, R1, R5 |  | IF | ID | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | IF | ID | EX | MEM | WB
LW R1, 0(R2) | IF | ID | EX | MEM | WB |  |  |  | 
SUB R4, R1, R5 |  | IF | ID | stall | EX | MEM | WB |  | 
AND R6, R1, R7 |  |  | IF | stall | ID | EX | MEM | WB | 
OR R8, R1, R9 |  |  |  | stall | IF | ID | EX | MEM | WB

## Slide 79: Forwarding
IF/ID
ID/EX
EX/MEM
MEM/WB
How would you design the forwarding?
Key idea: connect data internally before it's stored

## Slide 80: No Forwarding

## Slide 81: Data Hazard Solution: Forwarding
Key idea: connect data internally before it's stored
Assumption:
  The register file forwards values that are read and written during the same cycle.

## Slide 82: Data Hazard Summary
Three types of data hazards
  RAW (MIPS)
  WAW (not in MIPS)
  WAR (not in MIPS)
Solution to RAW in MIPS
  Stall
  Forwarding
    Detection & Control
      EX hazard
      MEM hazard
    A stall is needed if read a register after a load instruction that writes the same register.
  Reordering

## Slide 83: Data Hazard Solution: Forwarding
Key idea: connect data internally before it's stored
Assumption:
  The register file forwards values that are read and written during the same cycle.

## Slide 84: Forwarding
Add hardware to feed back ALU and MEM results to both ALU inputs
00
01
10
00
01
10

## Slide 85: Controlling Forwarding
Need to test when register numbers match in rs, rt, and rd fields stored in pipeline registers
"EX" hazard:
  EX/MEM - test whether instruction writes register file and examine rd register
  ID/EX - test whether instruction reads rs or rt register and matches rd register in EX/MEM
"MEM" hazard:
  MEM/WB - test whether instruction writes register file and examine rd (rt) register
  ID/EX - test whether instruction reads rs or rt register and matches rd (rt) register in EX/MEM

## Slide 86: Forwarding Unit Detail - EX Hazard
if (EX/MEM.RegWrite)
and (EX/MEM.RegisterRd ≠ 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
if (EX/MEM.RegWrite)
and (EX/MEM.RegisterRd ≠ 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10

## Slide 87: Forwarding Unit Detail - MEM Hazard
if (MEM/WB.RegWrite)
and (MEM/WB.RegisterRd ≠ 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
if (MEM/WB.RegWrite)
and (MEM/WB.RegisterRd ≠ 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 88: Data Hazards and Stalls
So far, we’ve only addressed “potential” data hazards, where the forwarding unit was able to detect and resolve them without affecting the performance of the pipeline.
There are also “unavoidable” data hazards, which the forwarding unit cannot resolve, and whose resolution does affect pipeline performance.
We thus add a (unavoidable) hazard detection unit, which detects them and introduces stalls to resolve them.

## Slide 89: Data Hazards & Stalls
Identify the true data hazard in this sequence:
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB
1 2 3 4 5 6

## Slide 90: Data Hazards & Stalls
Identify the true data hazard in this sequence:
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB
LW doesn’t write $s0 to Reg File until the end of CC5, but ADD reads $s0 from Reg File in CC3
1 2 3 4 5 6

## Slide 91: Data Hazards & Stalls
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB
EX/MEM forwarding won’t work, because the data isn’t loaded from memory until CC4 (so it’s not in EX/MEM register)
1 2 3 4 5 6

## Slide 92: Data Hazards & Stalls
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB
MEM/WB forwarding won’t work either, because ADD executes in CC4
1 2 3 4 5 6

## Slide 93: Data Hazards & Stalls: implementation
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB |  | 
 | IF | ID | ID | EX | MEM | WB
We must handle this hazard by “stalling” the pipeline for 1 Clock Cycle (bubble)
bubble
1 2 3 4 5 6

## Slide 94: Data Hazards & Stalls: implementation
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB |  | 
 | IF | ID | ID | EX | MEM | WB
We can then use MEM/WB forwarding, but of course there is still a performance loss
bubble
1 2 3 4 5 6

## Slide 95: Data Hazards & Stalls: implementation
Stall Implementation #1: Compiler detects hazard and inserts a NOP (no reg changes (SLL $0, $0, 0))
LW $s0, 100($t0) ;$s0 = memory value
NOP ;dummy instruction
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
NOP
ADD
IF | ID | EX | MEM | WB |  | 
 | IF | ID | EX | MEM | WB | 
 |  | IF | ID | EX | MEM | WB
bubble
bubble
bubble
bubble
bubble
Problem: we have to rely on the compiler
1 2 3 4 5 6

## Slide 96: Data Hazards & Stalls: implementation
Stall Implementation #2: Add a “hazard detection unit” to stall current instruction for 1 CC if:
ID-Stage Hazard Detection and Stall Condition:
If ((ID/EX.MemRead = 1) & ;only a LW reads mem
((ID/EX.RegRT = IF/ID.RegRS) || ;RS will read load dest (RT)
(ID/EX.RegRT = IF/ID.RegRT))) ;RT will read load dest
LW $s0, 100($t0) ;$s0 = memory value
ADD $t2, $s0, $t3 ;$t2 = $s0 + $t3
LW
ADD
IF | ID | EX | MEM | WB | 
 | IF | ID | EX | MEM | WB

## Slide 97: Data Hazards & Stalls: implementation
The effect of this stall will be to repeat the ID Stage of the current instruction. Then we do the MEM/WB forwarding on the next Clock Cycle
LW
ADD
IF | ID | EX | MEM | WB |  | 
 | IF | ID | ID | EX | MEM | WB
We do this by preserving the current values in IF/ID for use on the next Clock Cycle

## Slide 98: Data Hazards: A Classic Example
Identify the data dependencies in the following code. Which of them can be resolved through forwarding?
SUB $2, $1, $3
OR $12, $2, $5
SW $13, 100($2)
ADD $14, $2, $2
LW $15, 100($2)
ADD $4, $7, $15

## Slide 99: Data Hazards - Reordering Instructions
Assuming we have data forwarding, what are the hazards in this code? lw $t0, 0($t1) lw $t2, 4($t1) sw $t2, 0($t1) sw $t0, 4($t1)
Reorder instructions to remove hazard: lw $t0, 0($t1) lw $t2, 4($t1) sw $t0, 4($t1) sw $t2, 0($t1)

## Slide 100: Data Hazard Summary
Three types of data hazards
  RAW (MIPS)
  WAW (not in MIPS)
  WAR (not in MIPS)
Solution to RAW in MIPS
  Stall
  Forwarding
    Detection & Control
      EX hazard
      MEM hazard
    A stall is needed if read a register after a load instruction that writes the same register.
  Reordering

## Slide 101: Control Hazards
A control hazard is when we need to find the destination of a branch, and can’t fetch any new instructions until we know that destination.
A branch is either
  Taken: PC <= PC + 4 + Immediate
  Not Taken: PC <= PC + 4

## Slide 102: Control Hazard on Branches Three Stage Stall
Control Hazards
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
The penalty when branch take is 3 cycles!

## Slide 103: Branch Hazards
Just stalling for each branch is not practical
Common assumption: branch not taken
When assumption fails: flush three instructions

## Slide 104: Basic Pipelined Processor
In our original Design, branches have a penalty of 3 cycles

## Slide 105: Reducing Branch Delay
Move following to ID stage
a) Branch-target address calculation
b) Branch condition decision
Reduced penalty (1 cycle) when branch take!

## Slide 106: Reducing Branch Delay
Key idea: move branch logic to ID stage of pipeline
  New adder calculates branch target (PC + 4 + extend(IMM))
  New hardware tests rs == rt after register read
Reduced penalty (1 cycle) when branch take

## Slide 107: Control Hazard Solutions
Stall
  stop loading instructions until result is available
Predict
  assume an outcome and continue fetching (undo if prediction is wrong)
  lose cycles only on mis-prediction
Delayed branch
  specify in architecture that the instruction immediately following branch is always executed

## Slide 108
Branch Behavior in Programs
Based on SPEC benchmarks on DLX
  Branches occur with a frequency of 14% to 16% in integer programs and 3% to 12% in floating point programs.
  About 75% of the branches are forward branches
  60% of forward branches are taken
  80% of backward branches are taken
  67% of all branches are taken
Why are branches (especially backward branches) more likely to be taken than not taken?

## Slide 109: Static Branch Prediction
For every branch encountered during execution predict whether the branch will be taken or not taken.
Predicting branch not taken:
  Speculatively fetch and execute in-line instructions following the branch
  If prediction incorrect flush pipeline of speculated instructions
    Convert these instructions to NOPs by clearing pipeline registers
    These have not updated memory or registers at time of flush
Predicting branch taken:
  Speculatively fetch and execute instructions at the branch target address
  Useful only if target address known earlier than branch outcome
    May require stall cycles till target address known
    Flush pipeline if prediction is incorrect
    Must ensure that flushed instructions do not update memory/registers

## Slide 110: Control Hazard - Stall
beq
writes PC
here
new PC
used here

## Slide 111: Control Hazard - Correct Prediction
Fetch assuming
branch taken

## Slide 112: Control Hazard - Incorrect Prediction
“Squashed”
instruction

## Slide 113: 1-Bit Branch Prediction
Branch History Table (BHT): Lower bits of PC address index table of 1-bit values
  Says whether or not the branch was taken last time
  No address check (saves HW, but may not be the right branch)
  If prediction is wrong, invert prediction bit
a31a30…a11…a2a1a0
branch instruction
1K-entry BHT
10-bit index
0
1
1
prediction bit
Instruction memory
Hypothesis: branch will do the same again.
  1 = branch was last taken
  0 = branch was last not taken

## Slide 114: 1-Bit Branch Prediction
Example:
Consider a loop branch that is taken 9 times in a row and then not taken once. What is the prediction accuracy of the 1-bit predictor for this branch assuming only this branch ever changes its corresponding prediction bit?
  Answer: 80%. Because there are two mispredictions – one on the first iteration and one on the last iteration. Is this good enough and Why?

## Slide 115: 2-Bit Branch Prediction (Jim Smith, 1981)
Solution: a 2-bit scheme where prediction is changed only if mispredicted twice
  Red: stop, not taken
  Green: go, taken
T
T
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
11
10
01
00
T
NT
T
NT
NT

## Slide 116: n-bit Saturating Counter
Values: 0 ~ 2n-1
When the counter is greater than or equal to one-half of its maximum value, the branch is predicted as taken. Otherwise, not taken.
Studies have shown that the 2-bit predictors do almost as well, and thus most systems rely on 2-bit branch predictors.

## Slide 117: Control Hazards - Solutions
Delayed branches – code rearranged by compiler to place independent instruction after every branch (in delay slot).
add $R4,$R5,$R6
beq $R1,$R2,20
lw $R3,400($R0)
beq $R1,$R2,20
add $R4,$R5,$R6
lw $R3,400($R0)

## Slide 118: Summary - Control Hazard Solutions
Stall - stop fetching instr. until result is available
  Significant performance penalty
  Hardware required to stall
Predict - assume an outcome and continue fetching (undo if prediction is wrong)
  Performance penalty only when guess wrong
  Hardware required to "squash" instructions
Delayed branch - specify in architecture that following instruction is always executed
  Compiler re-orders instructions into delay slot
  Insert "NOP" (no-op) operations when can't use (~50%)
  This is how original MIPS worked